## Slide 1
pyEMS
Prof. Matteo V. Rocco
SESAM group
Department of Energy, Politecnico di Milano
Input-output general purpose system modelling framework

## Slide 2
Comparing modelling systems
pyESM purpose
Generating models from scratch
Application example
Package OOP structure
API reference
Outline

## Slide 3
Comparing modelling frameworks
Energy modelling frameworks
  Several packages already available (Calliope, OSeMOSYS, pyPSA, …)
  Open-source packages with high modelling capabilities
  Low flexibility (difficulties in developing modelling capabilities)
  Designed for end users (difficult to access and to customize model behavior)
General purpose modelling systems
  Shareware software available (mainly GAMS available)
  Platform to design models from scratch as LP problems
  High flexibility, time intensive (for experienced users)
  Designed for model developers
Databases handlers
  Few packages available (MARIO, pyMRIO)
  Open-source packages with nearly zero modelling capabilities

## Slide 4
pyESM purpose
Drawbacks of existing modelling frameworks
  Design oriented to end-users (low flexibility in designing new features or controlling models’ rationale)
  Unprofessional data management systems (no SQL-based databases)
  Difficulties in handling and inspecting data (no Business Intelligence support)
ESM
py
  SUT and IOT model generator
  Mathematical model defined as LP problem
  Mathematical model fully customizable by user
  Data management system based on SQLite
  Automatic generation of PowerBI reports
  Ideal for model end users and developers
https://github.com/MIMO-modelling-suite/pyesm.git
Desired features
  Flexibility (easy to implement model capabilities)
  Open source
  Design either for end-users and for developers/research
  Possibility to handle a variety of physical complexities
  Handling data like a pro

## Slide 5
Generating models from scratch
https://github.com/MIMO-modelling-suite/pyesm.git
Step 1
pyESM generates directory with default setup files
structure_sets.yml
structure_variables.yml
problem.yml
Step 2
User fills setup files, defining:
model sets
model variables
problem equations
Step 4
User fills excel files with exogenous model data.
Step 3
pyESM imports setup files and generates Model as Python object. Outputs:
Blank SQLite database
Excel raw data files
Step 5
pyESM performs the following actions:
Imports exogenosu data
Generates and solves numerical problems
Updates SQLite database
Generates PowerBI visual report

## Slide 6
A simple SUT model
  Mathematical model definition (sets, variables, symbolic problem)
gas power plant
Electricity
photovoltaic plant
Operational cost
households (final demand)
Sets definition
  Scenarios (s): “Reference”, “Energy transition”
  Time (y): five years
  Flows(f): “electricity, gas”, “electricity, pv”
  Flows, aggregated (f_agg): “electricity, gas”, “electricity, pv”
  Technologies (t): “gas power plant”, “photovoltaic plant”
  Costs (c): “operational costs”
Exogenous variables
  : market shares
  : technical coefficients
  : cost coefficients
  : final demand
  : special identity (constant)
SUT
Linear Programming model
Endogenous variables
  : total demand by flow
  : total demand by flow (aggregated)
  : total activity by technology
  : total operational costs

## Slide 7
A simple SUT model
Exogenosu variables
  : market shares
  : technical coefficients
  : cost coefficients
  : final demand
  : maximum allowed activity by technology
  : special identity (constant)
Endogenous variables
  : total demand by flow
  : total demand by flow (aggregated)
  : total activity by technology
  : total operational costs
  Linear Programming problem rationale:
  for each scenario, find the total activity by technology () that minimizes the overall total operational costs () the time horizon, complaining with the maximum allowed activity by technology (, assumed as a policy decision).
  For each scenario ():
  Total supply equals total demand
  Competition among electricity flows
  Industry-technology assumption
  Total operational costs
  Total activity constraint
  Positivity of decision variables
  Mathematical model definition (sets, variables, symbolic problem)

## Slide 8
Application example
Solving the example via pyESM
  Step 1 - pyESM generates directory with default setup files
  Step 2 - User fills setup files, defining model sets, variables, equations
  sets.yml
  variables.yml
  problem.yml

## Slide 9
Application example
Solving the example via pyESM
  Step 1 - pyESM generates directory with default setup files
  Step 2 - User fills setup files, defining model sets, variables, equations
  Step 3 - pyESM imports setup files and generates Model as Python object. Outputs: Blank SQLite database, Excel raw data files
  Step 4 - User fills excel files with exogenous model data.
  excel data file

## Slide 10
Application example
Solving the example via pyESM
  Step 1 - pyESM generates directory with default setup files
  Step 2 - User fills setup files, defining model sets, variables, equations
  Step 3 - pyESM imports setup files and generates Model as Python object. Outputs: Blank SQLite database, Excel raw data files
  Step 4 - User fills excel files with exogenous model data.
  Step 5 - pyESM imports exogenous data, generates and solves numerical problems, updates SQLite database, generates PowerBI report

## Slide 11
“default” directory:
default problems that can be replicated and used as templates to be customized
default files that are essential to configure the model.
“doc” directory:
includes documentation files (in progress)
includes other illustrative materials (presentations, examples, …)
“esm” directory:
base: directory including basic pyESM classes and methods
log_exc: logging and exceptions directory
support: includes util methods and ancillary classes necessary to handle files and SQLite database
“tests” directory includes pytest infrastructure
“tutorial.ipynb” jupyter notebook with examples and tutorials
Package OOP structure

## Slide 12
esm.base
.model.Model – main class of the package, with main methods accessible to users for creating/manipulating the model
.core.Core – inside Model class, composed by fundamental objects for the model
.index.Index – includes all fundamental information of the conceptual model (data tables, set tables, variables)
.set.DataTable – includes information about SQLite data tables (set coordinates, variables information, …)
.set.SetTable – includes information about SQLite set tables (e.g. technologies, products, …)
.variable.Variable – each instance is a model mathematical variable (use matrix, …)
.database.Database – class in charge of manipulating the SQLite database (data input/output interface with problem)
.problem.Problem – class in charge of manipulating conceptual and numerical problem
esm.log_exc.
exceptions – set of subclasses defining custom exceptions
logger.Logger – handle log messages during model execution
esm.support.
dotdict.Dotdict – ancillary class working as a normal dictionary but accessing keys with dot (.) notation
file_manager.FileManager – includes all methods to manipulate files (create, import, erase, …)
pbi_manager.PBIManager – includes all methods necessary to create and handle PowerBI report
sql_manager.SQLManager – includes all methods necessary to manage and operate on the SQLite database
util, util_constants – ancillary set of support functions (isolated functions)
esm.constants – essential constants required by all other modules
Package OOP structure

## Slide 13
Package OOP structure
Model()
PBIManager()
Core()
Logger()
SQLManager()
Logger()
FileManager()
Logger()
Index()
Database()
Problem()
Logger()
FileManager()
Logger()
FileManager()
Logger()
FileManager()
SQLManager()
Index()
Logger()
FileManager()
Index()
Set()
DataTable()
Logger()
Logger()
Logger()
esm.base.model.Model
Variable()
Logger()

## Slide 14
API reference
method esm.support.util.create_model_dir
“””
Create a directory structure for the generation of Model instances.
If no default_model is indicated, only basic setup files are generated.
Args:
model_dir_name (str): Name of the model directory.
main_dir_path (str): Path to the main directory where the model directory will be created.
default_model (str, optional): Name of the default modle to use as a template.
List of available templates in /src/constants.py. Defaults to None.
force_overwrite (bool, optional): if True, avoid asking permission to overwrite existing files/directories. Defaults to False.
”””

## Slide 15
API reference
main methods of class esm.base.model.Model
Method | Description
load_model_coordinates | Load information defined by user to the Index object inside the model (definition of sets and variables of the problem).
initialize_blank_database | Gerates SQLite database tables for sets and variables. Generates exogenous parameters input xlsx files.
load_data_files_to_database | Load user data (exogenous variables) to SQLite database.
initialize_problems | Define numerical problem as a series of cvxpy objects based on numerical data and user defined symbolic problem.
update_database_and_problem | In case of modification of exogenous data in xlsx files or symbolic problem, update SQLite database and numerical problem without re-casting Model instance.
run_model | Solve the defined numerical problems.
load_results_to_database | Exports endogenous results to SQLite database.
generate_pbi_report | Generates Power BI report

## Slide 16
ESM
py